## Slide 1: Lab 10 - UART

## Slide 2: Introduction - UART
Universal Asynchronous Receiver Transmitter
Each character (data byte) is placed in between the start and stop bits. The start bit is always 0 (low) and the stop bit is always 1 (high).
3 important components:
  Asynchronous transmitter
  Asynchronous receiver
  Baud rate generator

## Slide 3: Experiment Setup
PIC18F4520
TX pin
RX pin
Asynchronous Receiver
Asynchronous
Transmitter
green wire of TTL
white wire of TTL

## Slide 4: Asynchronous transmitter
Register bit needed to set:
TXEN (TXSTA<5>): Enable transmission.
SPEN (RCSTA<7>): Enable asynchronous serial port.
Register bit will set while transmit:
TRMT (TXSTA<7>): Read only, which is set when the TSR register is empty.
TXIF (PIR1<4>): Set when TXREG is empty
Reference: Datasheet p.211 FIGURE 18-3

## Slide 5: Asynchronous transmitter
Set up asynchronous transmission:
Set the baud rate correctly
Enable the asynchronous serial port by clearing SYNC (TXSTA<4>), and setting SPEN (RCSTA<7>)
If interrupt is desired, set TXIE (PIE<4>)
Enable the transmission by setting TXEN (TXSTA<5>), which will also set TXIF bit.
Load data to TXREG register to start transmission.
Reference: Datasheet p.214

## Slide 6: Asynchronous receiver
RCIF (RIR1<5>): will set when reception is complete
SPEN (RCSTA<7>): enable asynchronous serial port
OERR, FERR: error detect
CREN: continuous receive enable bit, will be cleared when error occurred
Reference: Datasheet p.213 FIGURE 18-6

## Slide 7: Asynchronous receiver
Set up asynchronous reception:
Set the baud rate correctly
Enable the asynchronous serial port by clearing SYNC (TXSTA<4>), and setting SPEN (RCSTA<7>)
If interrupt is desired, set RCIE (PIE<4>)
Enable the reception by setting bit, CREN (RCSTA<4>)
Read the 8-bit received data by reading the RCREG register
Reference: Datasheet p.216

## Slide 8: Baud Rate
BRG16 (BAUDCON<3>): choose 16-bit or 8-bit baud rate generator
  16-bit: SPBRGH and SPBRG
  8-bit: SPBRG only
SYNC (TXSTA<4>): EUSART Mode Select bit, we use async mode
BRGH (TXSTA<2>): High Baud Rate Select bit
SPBRGH : SPBRG: controls the period of a free-running timer
Reference: Datasheet p.206 EXAMPLE 18-1

## Slide 9: Baud Rate (Cont’)
Reference: Datasheet p.206 - 208

## Slide 10: Setting UART pin
The pins of the Enhanced UART are multiplexed with PORTC.
In order to configure RC6/TX/CK and RC7/TX/DT as a UART:
Bit SPEN (RCSTA<7>) must be set to 1
Bit TRISC <7> must be set to 1
Bit TRISC <6> must be set to 1.
Reference: Datasheet p.112 TABLE10-5

## Slide 11: Reference
PIC18F4520 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/39631E.pdf